## Slide 1: Measuring ECN generalization feasibility
Anna Maria Mandalari, Marcelo Bagnulo, Bob Briscoe, Andra Lutu
Sevilla, February 2017

## Slide 2: Outline
ECN generalization
  Why does it matter?
Testing ECN support
  Updated study / evolutionary study
Generalized ECN feasibility
  ECN in TCP control packets?
  Defining the tests of interest
  Measurement approach
    Measurement methodology, tools and platforms
Server ECN Congestion Behavior
  Methodology idea in implementation phase

## Slide 3: ECN overview (I)
ECN marking in IP header
  IP packets in an ECN TCP flow set the ECN Capable Transport (ECT) codepoint 0x01/0x10
  If a router detects congestion, it will mark the packet with Congestion Experience (CE) codepoint 0x11

## Slide 4: ECN overview (II)
ECN marking in TCP header
  Negotiation of ECN support in TCP 3-way handshake
  When receiving a packet marked with the CE codepoint, the destination host marks the TCP ECN Echo (ECE) in the packets it sends to the source
  Host receiving the packet with ECE mark reduces its congestion window and sends a packet with the Congestion Window Reduced (CWR) mark

## Slide 5: ECN generalization
[draft-bagnulo-tswg-generalized-ecn]
[RFC3168] Switches performing AQM can use ECN marks to signal congestion to the endpoints of a communication
  Precludes using ECN in TCP control packets (RFC 5562 -- SYN/ACK + ECT)
Data Center TCP (DCTCP) environment: non-ECT marked packets receive a penalty when they go through congested links
  Important to enable ECN marks on TCP control packets to increase the overall performance of the communication

## Slide 6: ECN generalization
[draft-bagnulo-tswg-generalized-ecn]
Test the path support for SYN+ECT, pure ACK + ECT, FIN + ECT
Revisit the support for SYN/ACK + ECT
What about TFO + SYN/ACK + ECT (may be too specific)

## Slide 7: Testing ECN Support
Medina-2004, Bauer-IMC11, Trammell-PAM2015
Support of server ECN in the wild
Path support for ECN marks (SYN, SYN/ACK)
Focus on web servers (e.g., Alexa top sites)
  Expand this to encompass other services:
    CDN networks (CDN brokers?)
    University networks

## Slide 8: Testing ECN Support
ECN in the wild: update on fraction of servers that negotiate ECN?
After TCP is negotiated, is ECT mark present at IP?
Upon sending artificial CE signal, do we observe the corresponding ECE?
TCP: SYN, ECE, CWR
TCP: SYN, ACK, ECE
TCP: ACK
IP: ECT
IP: CE
TCP: ECE

## Slide 9: Testing ECN Support
ECN Server Behavior in case of congestion
Upon receiving the ECE TCP mark, does the server reply with the CWR mark?
  How does the server reduce the congestion window? (cuts in half? – can we measure this?)
  Can we observe the CWR mark?
TCP: SYN, ECE, CWR
TCP: SYN, ACK, ECE
TCP: ACK
IP: CE
TCP: ECE
TCP: CWR

## Slide 10: Generalized ECN feasibility
RFC 5562, [draft-bagnulo-tswg-generalized-ecn]
SYN/ACK + ECT – check for servers that set the ECT on SYN/ACK (tomography-based approach)
  test ECE and non-ECE feedback from such servers
  testing for servers with TFO and ECN-capable SYN/ACKs?
  RFC5562 – why the 5way-handshake?
TCP: SYN, ECE, CWR
TCP: SYN, ACK
IP: ECT
TCP: SYN, ACK, ECE
IP: ECT --> CE
TCP: SYN, ECE, CWR
TCP: ACK, ECE

## Slide 11: Generalized ECN feasibility
SYN + ECT
  Does the server drop the SYN packet (silently or by sending RST)?
    Is RST, penalty is one RTT; otherwise, performance impacted
    Quantify prevalence in the wild
  Server replies with non-ECT marked SYN/ACK
    Conservative approach: reduce the congestion window
    Measure performance impact
  [Trammell-PAM15] - 0,82% of IPv4 sites and 0,61% of IPv6 sites fail to establish a connection when they receive a TCP SYN with any ECN codepoint set

## Slide 12: Generalized ECN feasibility
[draft-bagnulo-tswg-generalized-ecn]
SYN + ECT – testing path support using tracebox (tomography-based approach)
  SYN+ECE+CWR
  SYN+ECE+CWR+ECT(1)/ECT(0)
  SYN+ECE+CWR+CE
  Prevalence of paths stripping ECN
TCP: SYN, ECE, CWR
IP: ECT
TCP: SYN, ACK
IP: ECT
TCP: SYN, ACK, ECE
IP: ECT
TCP: SYN, ECE, CWR
IP: ECT --> CE

## Slide 13: Generalized ECN feasibility
[draft-bagnulo-tswg-generalized-ecn]
“Pure” ACK + ECT
Congestion on the ACK-path
  [RFC 3168] For the current generation of TCP congestion control algorithms, pure acknowledgement packets (e.g., packets that do not contain any accompanying data) MUST be sent with the not-ECT codepoint. Current TCP receivers have no mechanisms for reducing traffic on the ACK-path in response to congestion notification. Mechanisms for responding to congestion on the ACK-path are areas for current and future research. (One simple possibility would be for the sender to reduce its congestion window when it receives a pure ACK packet with the CE codepointset). For current TCP implementations, a single dropped ACK generally has only a very small effect on the TCP's sending rate.
IP: ECT
TCP: ACK
IP: ECT --> CE
TCP: ECE?

## Slide 14: Measurement Approach
Tools to use
  Pathspider
  Tracebox (inclining to use this for a tomography-based approach; information from pathspider may be redundant)

## Slide 15: Measurement Approach
We aim to use multiple platforms:
  Planetlab (700nodes available, working w a UIO account, no longer available – any chance for support on this from MAMI?)
  MONROE (at least one dev node per country, summing up 13 different MBB operators)
    Made some initial tests with my dev node in NO – but nothing sounds enough to report yet
  BISmark, CAIDA’s Ark? Other platforms?

## Slide 16: Questions?
Thank you!

## Slide 17: Backup slides

## Slide 18: Server ECN Congestion Behavior
Distribution of initial congestion window over the Alexa top 1M
  (IW10) upper bound for the initial window will be min (10*MSS, max (2*MSS, 14600))
  Set large rwnd, very small cwnd (e.g., MSS = 600B)
  Download home webpage and no ACK to the data => received bytes = init_cwnd
    Repeat several times, check distribution, select max.
  Once we know cwnd0, we can ACK the bytes and measure similarly the increased cwnd (cwnd1)
Test response to congestion signals from web servers
  3 duplicate ACKs
  Timeout
  ECE mark