## Slide 1
Enhancing encrypted transport protocols with passive measurement capabilities
Tobias Bühler, Mirja Kühlewind, Brian Trammell - ETH Zürich
TCP/IP
Cleartext header fields. TCP or higher level information is (mis)used for measurements. No proprietary measurement capabilities.
Encrypted (e.g. QUIC)
ACK frames and some header fields are encrypted. No packet matching is possible. E.g. RTT measurements are difficult for middleboxes.
Measurement Approaches
Transport Protocol Measurement Development
User Privacy
Low Protocol Overhead
Measurement Simplicity
Measurement Accuracy
Ease of Deployment
ACK
DATA
ACK
DATA
Conflicting Goals
Protocol provides measurement-specific data: Partially unencrypted wire image. Packet matching is possible. Examples are: Packet Number Echo, Spin Bit, additional flags
Track encrypted traffic: Use the observed encrypted packets/payloads to estimate e.g. RTT or packet loss. Possible techniques:
Use ML to learn traffic patters which can be used for measurements;
Infer measurements from coexisting TCP flows.
User/endpoints control the amount of dedicated measurement data and the time to expose this data. An endpoint could expose data if:
problems are detected (e.g. losses or high delay);
the user privacy is not influenced.
Operators still need measurements.
Real RTT
Additional delay
Estimated RTT
Sender
Receiver
Middlebox
Spin Bit = 0
Spin Bit = 1
Spin Bit = 0
Middlebox implementation: Using the Fast Data Project (FD.io): Fast data processing on generic hardware (in user space/C). Realistic performance.
Host A
Host B
Implementation
Endpoint implementation: Tests with an early QUIC implementation in Go and custom changes for e.g. packet number echo tests. Comparison with results based on TCP/IP flows.