PLUS (Work-In-Progress)
Roman Müntener, Stephan Neuhaus (ZHAW)

---
Implementation

---
Layering --- Traditional View
Application
Application
Transport
Transport
Network
Network
Network
Network
Medium Access
Medium Access
Medium Access
Medium Access
Physical
Physical
Physical
Physical

---
Layering With PLUS
- Crypto context needed for authentication of PLUS header material
- Works well with AEAD ciphers, probably not so well with more traditional auth (HMAC etc; insert personal rant about AEAD ciphers here)
- Also feedback channels, flags
Crypto
Context
Transport
Path (PLUS)
UDP/IP

---
Design Questions
- Would be possible to change implementation of transport layer to encompass PLUS, but that would be suboptimal. So:
- How do we design a reusable API for PLUS despite tight(ish) coupling between transport and PLUS?
- PLUS can not be treated as a wholly transparent layer
  - PLUS feedback channels/flags need cooperation from transport layer, e.g., S flag
  - OK, you can use defaults/compatibility layer, but you lose transport/PLUS interaction
- How do we make it easy to integrate into existing code?
- By making it as transparent as possible

---
About PLUS
- PLUS mandates encryption and integrity protection, also mandates that it uses overlaying transport for that
  - Needs help from transport layer implementation
- PLUS mandates feedback channels (MUST)
  - Should the PLUS code deal with feedback or should this be delegated to the transport layer code.
- PLUS introduces connection semantics
  - Should the PLUS code deal with ...
- Should these be as transparent as possible?
  - Compromise: Design the API to be usable either way.

---
API
- High level API
  - Provides connection objects that can be used by existing code as if it were a normal connection object
    - Thus handles connection multiplexing, encryption and PCF feedback/requests transparently
    - Implements net.Conn, so no flags, no feedback on that interface; of limited useablility
    - Connection object itself is of type plus.Connection, which has flags, feedback
- Low level API
  - Provides raw access to sending and receiving packets
  - does not perform connection multiplexing
  - encryption/integrity/pcf can be handled by transport layer completely if wanted (set callbacks to nil)

---
Crypto Context & Feedback Channel
- Each connection has a crypto context and a feedback channel provided by the transport layer.
- Crypto context needs to provide two methods:
  - EncryptAndProtect(header, payload): integrity protection and encryption.
  - DecryptAndValidate(header, payload): Perform integrity check and decryption.
- Feedback channel needs to provide one method:
  - SendFeedback(data): Sends data back as PCF feedback.

---
Control Flow
- Upon sending, the PLUS layer calls the crypto context’s EncryptAndProtect.
- Upon receiving, the PLUS layer calls the crypto context’s DecryptAndValidate.
- Upon receiving an extended header with a PCF request, the PLUS layer invokes the feedback channel’s SendFeedback.
- To send PCF feedback the outer layer will call the AddFeedback method provided by the PLUS layer.

---
Control Flow: New CAT
[Speaker Notes: The first packet could aready be encrypted and could already have a PCF request in it. Therefore, before the first data is delivered to the transport layer, crypto context and feedback channels need to be created]

---
Control Flow: Use of Existing Connection

---
Issues
- PLUS layer performs callbacks to the crypto context and feedback channel
  - Blocks all read operations ATM
  - Should be non-blocking
- PLUS layer may hold locks to internal state that should not be modified during these callbacks.
  - Callbacks should not attempt to read or send data from the connection and should only perform read access to the connection object’s internal state.
  - Otherwise deadlocking may occur.

---
Issues
- Callbacks may receive live buffers that can be modified safely as far as the PLUS layer is concerned, but outer layer might hold references to these buffers too
- It’s up to the outer layer to decide whether to modify buffers in callbacks directly or work on copies.
- Since encryption and integrity protection will likely require additional space, additional buffers will need to be allocated.
- To reduce the number of allocations, an outer layer may provide buffers to the Write methods that are large enough to hold additional data that is filled in in-place by the crypto context’s methods.
- writev-like API not possible because we use net.PacketConn
[Speaker Notes: Each write sends a separate UDP packet]

---
Issues
- A PLUS connection can be treated as a regular connection except that explicit stop signaling will not be possible as go’s net.Conn interface does not provide any methods to set PLUS flags
- PCF feedback handling will also not be possible.
- All existing protocols that will run (directly) on top of PLUS will have to be modified to account for PCF feedback handling.
[Speaker Notes: Net.Conn cannot send/receive feedback; need to do huge kludge to support this]

---
GUIC
- QUIC-GO (GUIC) has been modified to support PLUS
- We introduced a new frame type PLUSFeedbackFrame that is used to send feedback back
- We did not change anything to the crypto, meaning:
  - Crypto is as it was.
  - PLUS headers are not integrity protected.
- Uses the Low level API because GUIC has its own connection multiplexing mechanism (layer connection multiplexing is strange)
[Speaker Notes: QUIC crypto not easy to change, or even to refactor into CryptoContext object Possible in second step, or to switch to TLS]

---
Tools

---
plus-pcap
- Support added to gopacket to decode PLUS packets
- Command line tool plus-pcap using gopcap/gopacket
- Reads PCAP files containing PLUS packets or dumps traffic live
- Outputs JSON
[Speaker Notes: Gopacket fork, not merged]

---
pluspector
- Pluspector: A command line tool for debugging.
- Can relay connections (does not use raw sockets).
- Can generate packets and echo packets.
- Can generate packets and randomly modify bytes:
  - Serves as a trivial fuzzing tool to detect bugs.
- NOT a tool to debug transport protocols using PLUS.

---
plus-debug
- PDbg: A dummy protocol running on top of PLUS providing trivial encryption and integrity protection and packet retransmissions.
- Serves as a reference on how to use PLUS.
- Useful in testing.
- Not a production transport protocol. Encryption and integrity protection are deliberately very weak and packet retransmission is not designed to be efficient. Its sole purpose is in testing.

---
Open Questions

---
PCF
- Exact PCF mechanics and semantics: spec initially required to only send the non-integrity protected part (PCF value field) back, without PCF request type
- This was a problem because it made it impossible to know to what request this is feedback to and thus the type/format of the data remained unknown
- E.g. PCF requests are “hop count” and “MTU”, response is just “12” and “240”
- We decided that a receiver sends back the complete extended header instead