## Slide 1: Middlebox Measurement and Cooperation
Mirja Kühlewind and Brian Trammell, ETH Zürich
CleanSky Workshop Heidelberg, 29 Feb 2016

## Slide 2: Problem Statement: Ossification of the Internet due to Middlebox Impairments
Problem
Middleboxes make restrictive, implicit assumptions about traffic passing through them
  Deployment of "new" protocols/extension limited by packet/flow modifications of middleboxes
Goal
Reduce the accidental manipulation to zero, while minimizing the essential manipulation!
Needed
More data about the nature and distribution of middlebox impairments
  Common data model for storage and analysis of middlebox impairment
Explicit Middlebox cooperation to declare assumptions and intentions independent of the used transport or higher-layer protocol
  New (UDP-based) transport encapsulation + in-band signaling

## Slide 3: The MAMI Project Measurement and Architecture for a Middleboxed Internet
Strong interaction with relevant standards organizations for impact on deployment
FIRE testbed (MONROE) support for measurement as well as experimentation, especially on mobile broadband access networks
Learn more at http://mami-project.eu/
of deployed middleboxes
for middlebox cooperation
of use case applicability and deployability

## Slide 4: Middlebox Measurements: Golas and Overview
Large-scale measurements of path impairments
  using FIRE MONROE as well as RIPE Atlas, CAIDA Ark…
  UDP/TCP/SCTP connectivity, TCP options (e.g. TFO, MPTCP), and other protocol (ICMP, DNS, …)
Development of new measurements tools: https://github.com/mami-project/
  Tracebox: tracing + impairment analysis
  PathSpider: A/B testing (currently on ECN support)
Path Transparency Observatory
  Active measurements by the project + external measurements
  Query interface to access observations on path impairments:
    What is the likelihood that a certain path impairment impacts my traffic (modifications/stripping/dropping/blocking)?

## Slide 5: Path Transparency Observatory
Observatory (public release end 2016) to derive common observations about conditions on a given path at a given time
Combining disparate measurements leads to better insight
  e.g. own measurement data, traceroutes, BGP, traces
Follow http://mami-project.eu for availability!
active A/B test
(PathSpider)
traceroute
mod trace
(tracebox)
looking glass
etc.
observations
{t,p,c,v}
preanalysis
preanalysis

## Slide 6: Is it possible to run the Internet over UDP? Preliminary Results
A/B testing for TCP/UDP connectivity
  Copycat tool on 120 PlanetLab nodes
      3,67% UDP blocking on port 33435
      2,7% UDP blocking on all tested ports (33435,1228, 8008, 12345)
  RIPE Atlas traceroute
      3.661% UDP blocking based on existing traceroutes
We are currently running more measurements!
  Use all existing testbeds available, e.g. CAIDA Ark, MONROE

## Slide 7: Middlebox Cooperation: Architectural Considerations
Shim for Middlebox Cooperation Protocol (MCP)
  Transport and applications can selectively expose semantic information to middlebox
  Higher layers can fully be encrypted
Flexible Transport Layer (FTL)
  Maintain connectivity (even if the MCP is not supported) e.g. fallback or happy-eyeball mechanisms
  Provision of encryption context for different layers/protocols

## Slide 8: Problem Statement
Deployment problems of new protocols and protocol extension due to ossification in the Internet, e.g.
  Multipath TCP
  QUIC (over UDP)
Operation and management of in-network functionality hindered due to increasing deployment of encryption, e.g.
  firewalls using port mapping or DPI
  performance enhancements in mobile networks

## Slide 9: Why a new shim?
Transport layer: end-to-end sockets
  flow information
Internet layer: hop-by-hop handling
  per-packet information
  stateless and simple processing in the middle
  stateful and ‚smart‘ processing at the edge
Missing:
Per-flow information for
stateful in-network functions
Path layer for explicit cooperation with middleboxes instead of implicit assumptions

## Slide 10: Path Layer: (Basic) Functional Requirements
Grouping of packets into flows
Extensibility to provide per-flow network information
Explicit feedback channel
resv
tube/group/flow id
checksum
option space …
magic

## Slide 11: Example 1: Firewall Traversal
Problem
    UDP often blocked as it is hard to maintain state
Needed
  group ID
  start/stop signal and confirmation by receiver (‚SYN/ACK’)
Action
  firewall can forward first packet and set up state based on confirmation from receiver
  group ID must be large enough to not be guessable

## Slide 12: Example 2: Low Latency Support
Problem
    Network service not optimized for latency sensitive traffic
Needed
    Flag to signal loss sensitivity vs. latency sensitivity
Action
  network device can treat latency sensitive traffic differently, e.g. in a separate smaller queue
  trade-off between loss and latency gives not incentive to lie

## Slide 13: Why should I trust what you say about your flows?
Default: trust but verify
  declarative signaling: no negotiation, no guarantees
  the best way to prevent cheating is to make it useless to do so
Leverage existing trust relationships for higher-assurance declarations
  e.g. your enterprise firewall, access network middleboxes, etc.

## Slide 14: Will it deploy?
Transport-layer encapsulation over UDP
  Need ports for NAT
  Impossible to deploy with new protocol number across the Internet
  Userspace (and kernelspace) implementation possible
Magic number for easy recognition, protection against reflection
Flags for “SYN/ACK” condition for state decision delegation to endpoint
  All traffic bidirectional
  Data in first packet possible
Signals fit in a single packet (no segmentation or reliability)
Checksum for error detection, cryptographic integrity checks available

## Slide 15: Implementing an Explicit Path Interface
Application can directly indicate requirements to path layer
Transport can use the path layer to expose parts of its functionality/intentions to the network
Middlebox Cooperation protocol (MCP) signals these information appropriately to on-path middleboxes

## Slide 16: References
Substrate Protocol for User Datagrams (SPUD) in the IETF
  draft-trammell-spud-req
  draft-kuehlewind-spud-use-cases
  draft-hildebrand-spud-prototype
IAB Stack Evolution Program
  Workshop on Stack Evolution in a Middlebox Internet (SEMI) 2015 [RFC7663]
  B. Trammell, J. Hildebrand: Evolving Transport in the Internet
IRTF proposed research group on Measurement and Analysis for Protocols (MAPRG)
MAMI webpage (mami-project.eu) or twitter (@mamiproject)

## Slide 17: Summary and Conclusion
Problem
Ossification of the Internet Protocol Stack
Needed
Measurement to identify path impairments
  Large-scale using all available testbeds (incl. MONROE)
  New measurements tools (Tracebox, PathSpider)
  Path Transparency Observatory
Path layer for explicit middlebox cooperation
  Middlebox Cooperation Protocol (MCP): trust by verify
  Encrypted everything else!