## Slide 1
An Observatory for Internet Path Transparency
Mirja Kühlewind and Brian Trammell, ETH Zürich
Raw metadata includes
file format definition and
owner contact information.
Analysis metadata includes commit-specific reference to platform-independent sources.
Observations are grouped into observation sets, which share common provenance.
Observation set metadata links to observations and raw data files from which they are derived, plus analysis that produced them.
Queries can be made permanently cacheable, and metadata links to observation sets involved in query results.
Rampant deployment of middleboxes means the Internet is no longer end-to-end.
New protocols and protocol extensions need to work around impairments on path
These efforts should be guided by data about relative prevalence of these impairments.
How to make this data available to networking research and operations communities?
→ build an open repository around a common data model for comparable and repeatable measurement of these phenomena.
Observation: an assertion that at a given time along a given path, a given condition held:
Conditions are defined in a structured namespace oriented to assign states to aspects of attempts to use a given protocol feature, fostering comparability of results.
Every object stored in the observatory, including queries, keeps its provenance, including arbitrary metadata, fostering measurement repeatability.
Paths are defined as sequences of elements (addresses, prefixes, BGP ASN, pseudonyms), allowing multi-resolution storage and correlation with topographic information (e.g. Tracebox)
[IP0 * IP8] → [IP0 IP1 AS3 * AS5 IP6 * IP8]
The PTO is implemented as a RESTful API, storing raw data files organized into campaigns, normalizing these into a queryable observation database.
Deploying soon: https://observatory.mami-project.eu/ — code: https://github.com/mami-project/pto3-go
O = {t, p, c}