## Slide 1: A Vision for Explicit Path-Cooperative Transport
Mirja Kühlewind and Brian Trammell, ETH Zürich Joe Hildebrand, Cisco Systems
Innovations in Clouds, Internet, and Networks Paris, 1 March 2016

## Slide 2: The MAMI Project Measurement and Architecture for a Middleboxed Internet
Strong interaction with relevant standards organizations for impact on deployment
FIRE testbed (MONROE) support for measurement as well as experimentation, especially on mobile broadband access networks
Learn more at http://mami-project.eu/
of deployed middleboxes
for middlebox cooperation
of use case applicability and deployability

## Slide 3: Overview
Why do we need explicit middlebox cooperation?
Why do we need a shim layer for this?
Is it deployable?
How do we have to design the protocol to make it deployable?

## Slide 4: Why explicit middlebox cooperation?
Deployment problems of new protocols and protocol extension due to ossification in the Internet, e.g.
  Multipath TCP
  QUIC (over UDP)
Operation and management of in-network functionality hindered due to increasing deployment of encryption, e.g.
  firewalls using port mapping or DPI
  performance enhancements in mobile networks

## Slide 5: Why a new shim layer?
Transport layer: end-to-end sockets
  flow information
Internet layer: hop-by-hop handling
  per-packet information
  stateless and simple processing in the middle
  stateful and ‚smart‘ processing at the edge
Missing:
Per-flow information for
stateful in-network functions
Path layer for explicit cooperation with middleboxes instead of implicit assumptions

## Slide 6: Path Layer: (Basic) Functional Requirements
Grouping of packets into flows
Extensibility to provide per-flow network information
Explicit feedback channel from middlebox to endpoint
group/tube/flow id
resv
checksum
option space …
magic

## Slide 7: Why should I trust what you say about your flows?
Default: trust but verify
  declarative signaling: no negotiation, no guarantees
  the best way to prevent cheating is to make it useless to do so
  minimize the information exposed!
Leverage existing trust relationships for higher-assurance declarations
  e.g. your enterprise firewall, access network middleboxes, etc.

## Slide 8: Example 1: Firewall Traversal
Problem
    UDP often blocked as it is hard to maintain state
Needed
  group ID
  start/stop signal and confirmation by receiver (‚SYN/ACK’)
Action
  firewall can forward first packet and set up state based on confirmation from receiver
  group ID must be large enough to not be guessable

## Slide 9: Example 2: Low Latency Support
Problem
    Network service not optimized for latency sensitive traffic
Needed
    Flag to signal loss sensitivity vs. latency sensitivity
Action
  network device can treat latency sensitive traffic differently, e.g. in a separate smaller queue
  trade-off between loss and latency gives no incentive to lie

## Slide 10: Will it deploy?
Transport-layer encapsulation over UDP
  Need ports for NAT
  Impossible to deploy with new protocol number across the Internet
  Userspace (and kernelspace) implementation possible
Magic number for easy recognition, protection against reflection
Flags for “SYN/ACK” condition for state decision delegation to endpoint
  All traffic bidirectional
  Data in first packet possible
Signals fit in a single packet (no segmentation or reliability)
Checksum for error detection, cryptographic integrity checks available

## Slide 11: Implementing an Explicit Path Interface
Application can directly indicate requirements to path layer
Transport can use the path layer to expose parts of its functionality/intentions to the network
Middlebox Cooperation protocol (MCP) signals these information appropriately to on-path middleboxes
Minimize the information exposed!

## Slide 12: Is it possible to run the Internet over UDP? Preliminary Results
A/B testing for TCP/UDP connectivity
  Copycat tool on 120 PlanetLab nodes
      3,67% UDP blocking on port 33435
      2,7% UDP blocking on all tested ports (33435,1228, 8008, 12345)
  RIPE Atlas traceroute
      3.661% UDP blocking based on existing traceroutes
We are currently running more measurements!
  Use all existing testbeds available, e.g. CAIDA Ark, MONROE
  Other impairment measurements: TCP Options, SCTP, …

## Slide 13: Path Transparency Observatory
Observatory (public release end 2016) to derive common observations about conditions on a given path at a given time
  Active measurements, made by the project
  External measurements (e.g. traceroutes, BGP, traces)
Combining disparate measurements leads to better insight
  How likely is it that a certain path impairment impacts my traffic?
Follow http://mami-project.eu for updates on data model & availability!
active A/B test
(PathSpider)
traceroute
mod trace
(tracebox)
looking glass
etc.
observations
{t,p,c,v}
preanalysis
preanalysis

## Slide 14: References
Substrate Protocol for User Datagrams (SPUD) in the IETF: spud@ietf.org
  draft-trammell-spud-req
  draft-kuehlewind-spud-use-cases
  draft-hildebrand-spud-prototype
IAB Stack Evolution Program
  Workshop on Stack Evolution in a Middlebox Internet (SEMI) 2015 [RFC7663]
  B. Trammell, J. Hildebrand: Evolving Transport in the Internet
IRTF research group on Measurement and Analysis for Protocols (MAPRG): maprg@irtf.org
MAMI webpage (mami-project.eu) or twitter (@mamiproject)