## Slide 1
of deployed middleboxes
for middlebox cooperation
for Internet-scale deployability
measurement
architecture
experimentation
Large-scale measurements of path impairments
  using FIRE MONROE as well as RIPE Atlas, CAIDA Ark…
  UDP/TCP/SCTP connectivity, TCP options (e.g. TFO, MPTCP), and other protocol (ICMP, DNS, …)
Development of new measurement tools
https://github.com/mami-project/
  Tracebox: tracing + impairment analysis
  Copycat: TCP/UDP differential on-path treatment
  PathSpider: A/B testing (currently on ECN support)
Path Transparency Observatory
  Active measurements by the project + external measurements
  Public query interface (end 2016) to access path impairment data:
  What is the likelihood that a certain path impairment impacts my traffic (modifications/stripping/dropping/blocking)?
  Common data model for all observations of path conditions
  t: time of observation
  p: path to which observation applies
  c: condition observed, e.g. “feature X  packet loss”
  v: vector of condition-specific values
Shim for Middlebox Cooperation Protocol (MCP)
  Transport and applications can selectively expose semantic information to middleboxes
  Higher layers can be fully encrypted!
  Implements a path layer within the Internet architecture
Flexible Transport Layer (FTL)
  Maintain connectivity (even if the MCP is not supported) e.g. via fallback or happy-eyeball mechanisms
  Provision of encryption context for different layers/protocols
  API with explicit support for the path as a first-order concept
Focus on standardization activities
  for coordination with industry and transition to practice (IETF Transport Area, IAB Stack Evolution Program)
Missing:
Per-flow information for
stateful in-network functions
Implementation and testing of MCP/TLF software
  Testing applicability of MCP in the Internet
  Functional testing of middlebox implementation in a NFV- based network
Focus on current challenges to the Internet
  Congestion management in 4G/5G networks
  Low latency support for end-to-end applications
  Gateways for in-network privacy protection
Leveraging FIRE testbeds for real-world experience
  MONROE provides access to a variety of European broadband and mobile carriers
active A/B test
(PathSpider)
traceroute
mod trace
(tracebox)
looking glass
etc.
observations
{t,p,c,v}
preanalysis
preanalysis
To understand middlebox impairment,
we must first measure it.
Then we adjust the Internet architecture
for explicit cooperation with path elements
Finally, we verify that new protocols
can coexist and be incrementally deployed
in today’s Internet
Learn more, and follow our progress: https://mami-project.eu
The end-to-end
ideal
Today’s middleboxed
reality