Oh, And One More Thing...

---
Implementation

---
Design Questions
- How do we separate a layer into two layers?
  - PLUS can not be treated as a transparent layer.
- How do we make it easy to integrate into existing code?
  - By making it a transparent layer?

---
About PLUS
- PLUS mandates encryption and integrity protection
  - Should the PLUS code deal with encryption/integrity or should this be delegated to the outer layer code.
- PLUS mandates feedback channels
  - Should PLUS code deal with …
- PLUS introduces connection semantics.
  - Should the PLUS code deal with ...
- Should these be as transparent as possible?
  - Compromise: Design the API to be usable either way.

---
API
- High level API
  - Provides connection objects that can be used by existing code as if it were a normal connection object (like TCP).
    - Thus handles connection multiplexing, encryption and PCF feedback/requests transparently.
- Low level API
  - Provides raw access to sending and receiving packets, does not perform connection multiplexing, encryption/integrity/pcf can be handled by the outer layer completely if wanted.

---
Crypto Context & Feedback Channel
- Each connection has a crypto context and a feedback channel provided by the outer layer.
- Crypto context needs to provide two methods:
  - EncryptAndProtect(header, payload): Perform integrity protection and encryption.
  - DecryptAndValidate(header, payload): Perform integrity check and decryption.
- Feedback channel needs to provide one method:
  - SendFeedback(data): Sends data back as PCF feedback.

---
Control Flow
- Upon sending the PLUS layer calls the crypto context’s EncryptAndProtect.
- Upon receiving the PLUS layer calls the crypto context’s DecryptAndValidate.
- Upon receiving an extended header with a PCF request the PLUS layer invokes the feedback channel’s SendFeedback.
- Upon receiving PCF feedback the outer layer will call the AddFeedback method provided by the PLUS layer.

---
Control Flow
Receiving an extended packet with a new CAT:

---
Issues
The PLUS layer performs callbacks to the crypto context and feedback channel which means that these methods should be non-blocking. The PLUS layer may hold locks to internal state that should not be modified during these callbacks. Thus: Callbacks should not attempt to read or send data from the connection and should only perform read access to the connection object’s internal state. Otherwise deadlocking may occur.

---
Issues
- These callbacks may receive live buffers that can be modified safely as far as the PLUS layer is concerned. However, the outer layer might hold references to these buffers too. It’s up to the outer layer to decide whether to modify buffers in callbacks directly or work on copies.
- Since integrity protection likely requires additional space buffers will need to be allocated. To reduce the number of allocations an outer layer may provide buffers to the Write methods that are large enough to hold additional data that is filled in in-place by the crypto context’s methods.

---
Issues
- Due to the crypto context and feedback channel a PLUS connection can be treated as a regular connection WITH the exception that explicit stop signaling will not be possible as go’s net.Conn interface does not provide any methods to set PLUS flags as well as PCF feedback handling will not be possible.
- ALL existing protocols that will run (directly) on top of PLUS will have to be modified to account for PCF feedback handling.

---
GUIC
- QUIC-GO (GUIC) has been modified to support PLUS.
  - We introduced a new frame type PLUSFeedbackFrame that is used to send feedback back.
  - We did not change anything to the crypto meaning:
    - Crypto is as it was.
    - PLUS headers are not integrity protected.
  - Uses the Low level API because GUIC has it’s own connection multiplexing mechanism and layer connection multiplexing is strange.

---
Tools

---
plus-pcap
- We added support to gopacket to decode PLUS packets.
- We wrote a command line tool (plus-pcap) using gopcap/gopacket to be able to read PCAP files containing PLUS packets or dump traffic live.
  - Output format is JSON.

---
pluspector
- Pluspector: A command line tool for debugging.
  - Can relay connections (does not use raw sockets).
  - Can generate packets and echo packets.
  - Can generate packets and randomly modify bytes:
    - Serves as a trivial fuzzing tool to detect bugs.
  - NOT a tool to debug transport protocols using PLUS.

---
plus-debug
- PDbg: A dummy protocol running on top of PLUS providing trivial encryption and integrity protection and packet retransmissions.
  - Serves as a reference on how to use PLUS.
  - Useful in testing.
  - It is not a production transport protocol. Encryption and integrity protection is deliberately very weak and packet retransmission is not designed to be efficient. Its sole purpose is in testing.

---
Open Questions

---
PCF
- Exact PCF mechanics and semantics.
  - The spec initially required to only send the non-integrity protected part back. This was a problem because it made it impossible to know to what request this is feedback to and thus the type/format of the data remained unknown.
  - It was decided that a receiver sends back the complete extended header instead.